Setting up your projector, elmo and laptop

Look at the following diagrams to set up your projector, Elmo and notebook computer.

You will need five items:  1. your projector; 2. your Elmo; 3. your computer; and 4. two connecting cables.  The two cables are the same on both ends, so it does not matter end you plug in.

The steps to connect and activate the setup are:

1. Connect your Elmo to your projector – connect the first cable to the RGB out port on the Elmo and plug the cable into the computer in port of the projector.

2. Connect your computer to the Elmo – connect the second cable to the RGB in port of your Elmo and plug the other end of the cable into the video (screen icon) port of the computer.

You are not quite done.  After you have connected the three components with the two cables, make sure to:

1.  Power on the Elmo and press the Document camera button to project from your Elmo.

2.  To switch from the Elmo to the laptop, press the Laptop button on the Elmo.  The signal will then pass from the computer, through the Elmo to the projector.

3.  If no image appears, hold down the Fn key on your laptop and then tap the F7 key that has the screen icon on it.  This will give you a dialog box that allows you to set your laptop to project its screen image.